## Slide 1
Latency and Frame Rate
Six-camera EO / IR panorama · V19 Milestone 1
Measured three independent ways: the RTL and its simulation, an in-fabric timing probe read over JTAG, and the SDI output captured and analysed frame by frame.
RTL + simulation
ILA / in-fabric probe
Optical capture (Python)
2026-08-20

## Slide 2
SUMMARY
What the system does today
30
frames/s published
IR single
30
frames/s published
IR panorama
30
frames/s published
EO single, all six
22.9
frames/s published
EO panorama
71 ms
capture to display
EO panorama, best
Latency is a fixed number per mode, not a range
Every row of the picture has the SAME capture-to-display latency. A row captured early waits longest for its frame to complete, and is then scanned out first; a row captured last waits least and is scanned out last. The two offsets cancel exactly. This is shown on the next slide and is the reason no "typical" figure appears anywhere in this deck: there is no spread to average over.
Where the remaining work is
Seven of the eight measured configurations publish at the rate their cameras produce. EO panorama publishes 22.9 against a 30 fps source: 78% of its frames arrive on the full 33.3 ms cadence and 22% slip by one or two frame periods. The cause is identified and is not the output stage - see the last two slides.
Frame rates: optical measurement, 2026-08-20, three-bank build 00e0c57. Latency: in-fabric timing probe, 2026-08-19, build 67955bc. Both are identified on the basis slide.

## Slide 3
THE KEY PICTURE
Why the stages must not be added up
Capture, render and scan-out overlap. Drawn end to end they read as 105 ms; drawn against one clock they are 71.5 ms.
0.0
33.3
66.7
100.0
milliseconds — one shared clock
Display frame edges
Camera exposes and transfers
frame N row 0 first → row 1079 last
FPGA aligns, renders, writes
align + render into a free bank
Published on the next edge
Display scans the frame out
row 0 first → row 1079 last
frame complete
published
row 0 → 71.5 ms
row 1079 → 71.5 ms
same length,
different start
The arithmetic. For row r of N: age when the frame completes = (1 − r/N) × 33.3, scan-out position = (r/N) × 33.3. These sum to 33.3 for every r — the row that waits longest to be captured is displayed first. Total = 33.3 + render-and-publish, identical for every row. Checked over all 1080 rows: spread 0.00 ms.
Notes: Exact for the single-camera modes, where output row r comes from source row r. In the panorama modes the warp lets a source row land within a band of output rows, so the cancellation is approximate - bounded by the row-window span of about 13 source rows, under 0.5 ms.

## Slide 4
MEASURED
Latency: best case and worst case
A finished frame may only be published on a display frame edge, and the camera does not track the display. The wait for that edge is anywhere from nothing to a full frame period, and that is the entire difference between the two columns.
Mode
Render occupancy
(ILA, untriggered)
Frame → render done
= fixed wait + render
BEST CASE
capture → display
WORST CASE
capture → display
Publishing when
this was measured
EO single
~8.4 ms
10.1 ms
43.4 ms
76.8 ms
29.75 fps
EO panorama
~24.9 ms
38.2 ms
71.5 ms
104.9 ms
15.03 fps
IR single
not measured
25.8 ms
59.1 ms
92.5 ms
30.01 fps
IR panorama
~26.6 ms
41.6 ms
74.9 ms
108.3 ms
15.03 fps
Why 41.6 ms does not cap throughput at 24 fps
The middle column is a latency, not an occupancy. It is a fixed phase wait plus the render — for IR panorama, about 15 ms of waiting for the row window to open, then a 26.6 ms render.
Only the render occupies the engine, and 26.6 ms fits inside 33.3 ms. The wait is a constant offset: it delays every frame equally and costs nothing per frame. Renders never overlap, so throughput is set by the occupancy alone.
Why the worst case occurs
The render finishes at some moment inside the display's 33.3 ms cycle and cannot choose that moment. Finish just before an edge and the frame goes out at once; finish just after one and it is held a whole further period.
This is a continuous drift, not an occasional fault — which is why no single "typical" value is quoted. Shortening the render moves both columns down; locking the camera to the display raster would collapse them to one.
Scope of the two flagged rows. Both panorama latencies were measured on the main branch while those modes published 15 fps. The 30 fps and 22.9 fps figures elsewhere in this deck come from the IR-DDR branch, which feeds IR panorama through DDR input buffers instead of live line caches. The render occupancies still fit 33.3 ms, so these bounds remain the best available, but they have not been re-measured on the branch that achieves 30 fps.
Notes: The IR panorama reference event read 15 Hz in that capture where the genlock says 30 - already recorded as untrustworthy in MEASURED_20260819. Re-measuring latency on the IR-DDR branch needs the timing probe ported to it; that branch has never carried it.

## Slide 5
MECHANISM
Best and worst, drawn on the same clock
Identical camera, identical render. The only difference is where the display's edge grid happens to fall — which nothing in the system controls.
BEST CASE — the render lands just before an edge
Display edges
Camera frame N
Align + render
38.2 ms
On screen
71.5 ms after capture
published
WORST CASE — the same render lands just after one
Display edges
Camera frame N
Align + render
38.2 ms — the same
Held, then on screen
held a whole frame period
104.9 ms after capture
edge missed by 0.35 ms
next edge
0.0
33.3
66.7
100.0
133.3
With the earlier two-bank output framebuffer a missed edge cost more than a late frame: the frame waiting to be published also blocked the NEXT render from starting, so one miss threw away a whole camera frame and the mode settled at half rate. The third output bank removes that blocking - the render behind it now proceeds regardless.

## Slide 6
OPTICAL EVIDENCE
Frame rate, measured off the SDI output
Grab the output at 60 fps, hash each frame, and count how often the picture changes. Repeat runs of 2 mean 30 fps; runs of 4 mean 15.
Mode
Camera delivers
New frames/s on screen
Repeat-run distribution
Verdict
IR single
30
29.81
2 × 352
at source rate
IR panorama
30
29.97
2 × 359
at source rate
EO single cam 1
30
29.89
2 × 357
at source rate
EO single cam 2
30
29.06
2 × 337, 4 × 11
at source rate
EO single cam 3
30
29.23
2 × 344, 4 × 5
at source rate
EO single cam 4
30
29.56
2 × 349, 4 × 5
at source rate
EO single cam 5
30
29.73
2 × 356, 4 × 2
at source rate
EO single cam 6
30
29.56
2 × 351, 4 × 4
at source rate
EO panorama
30
22.90
2 × 274, 4 × 55, 6 × 22
22% of frames slip
The instrument was checked before the results were believed. A USB3 capture card can duplicate or drop frames on its own. IR single returns repeat runs of exactly 2 at a 59.9 fps grab, 352 times in a row, so the card resolves 30 distinct frames per second cleanly. Lower resolution and MJPEG change nothing. A duplicate would hash the same and count once; a dropped frame would make this under-count, never over-count.

## Slide 7
WHERE THE LIMIT WAS WRITTEN
Evidence 1 — the RTL
The output framebuffer held two banks. A finished frame occupied one until it was displayed, and the rule below refused to start another render until then.
BEFORE
wire copy_bank_available =
!pending_valid &&
(!frame_valid || (wr_bank != rd_bank));
// !pending_valid = "nothing is waiting to be shown"
AFTER
wire [2:0] out_bank_busy =
(1 << rd_bank) |
(pending_valid ? (1 << pending_bank) : 0);
// three banks, so a free one always exists
Why that rule cost a whole frame rather than a few milliseconds
A render cannot be started whenever convenient — its start is locked to the source. For IR panorama the renderer reads the live camera line caches, so it may only begin while the row gate is satisfied:
wire row_window_ok = (rows_max <= gate_min_row + 30);
wire row_ready_now = (rows_min >= need_row) && row_window_ok;
// rows 34..64 of 512 -> 1.95 ms, once per 33.3 ms camera frame
Miss that 1.95 ms window and the next chance is a full camera frame away. That is how a few milliseconds of commit delay turned into exactly half rate.
src/PanoramaBase_DdrBlackFrame.v and src/IrV19StreamingRenderer.v. The third bank required moving one address region; it was moved by exactly 8100 × 128 addresses so every camera keeps its DRAM bank assignment.

## Slide 8
REPRODUCED, NOT ASSUMED
Evidence 2 — simulation across the phase
The offset between the camera clock and the display clock is not adjustable on hardware, so it was swept in simulation. Render 26.6 ms against a 33.3 ms frame edge.
Camera-to-display phase
TWO banks
fps
source frames
lost
THREE banks
fps
source frames
lost
0 µs
29.85
0
29.85
0
4 166 µs
30.00
0
30.00
0
8 332 µs
15.00
100 of 200
29.85
0
12 498 µs
15.00
100 of 200
29.85
0
16 664 µs
15.00
100 of 200
29.85
0
20 830 µs
15.00
100 of 200
29.85
0
24 996 µs
15.00
100 of 200
29.85
0
29 162 µs
15.00
100 of 200
29.85
0
6 of 8
phases lose exactly half the source frames with two banks
0 of 8
lose anything with three banks, and no bank is ever written while displayed
The two phases that already worked are the ones where the display edge happens to fall in the narrow gap between the render finishing and the next source window opening. That is the stated mechanism reproducing itself, which is what makes this a demonstration rather than an argument.
sim/tb_V19OutputBankRate.v. The same testbench asserts on every render start that the chosen bank is neither being displayed nor holding an unshown frame: zero violations across all sixteen configurations.

## Slide 9
ILA
Evidence 3 — the in-fabric timing probe
An ILA window is 8.8 µs and carries no timestamps, so a 33 ms interval cannot be recovered from a capture however it is triggered. The intervals are therefore measured in the FPGA and only the results are read out.
V19TimingProbe u_v19_timing (
.in_frame_ev (camera frame available),
.copy_start_ev(render begins),
.copy_done_ev (render complete),
.commit_ev (published to the display),
.out_edge_ev (output raster boundary));
// tick = ui_clk / 64 = 274.2 ns, 24 bits = 4.6 s
Measured intervals
Mode
frame → render done
(wait + render)
frame → on screen
EO single
10.1 ms
16.4 ms
EO panorama
38.2 ms
41.1 ms
IR single
25.8 ms
50.1 ms
IR panorama
41.6 ms
45.0 ms
Two ways this measurement lied before it was trusted
A capture triggered on activity cannot see idleness
Arming the ILA on "render active" reported the render occupying 84% of every frame. Sampling with no trigger condition at all gave 25-40%. Every duty figure in this deck is from an untriggered capture.
An interval register reports the LAST interval, not a rate
A pipeline that has stopped keeps reporting whatever it last managed - one stalled mode read as a healthy 33.3 ms while publishing nothing. Rates here are counted over a wall-clock gap, or measured optically, never read from an interval.
src/V19TimingProbe.v, calibrated against known intervals in sim/tb_V19TimingProbe.v — 10 of 10 checks pass. Captures via scripts/capture_v19_untriggered.tcl.

## Slide 10
PYTHON / OPTICAL
Evidence 4 — the output, analysed frame by frame
The FPGA counter says a frame was published. Only this says the picture actually changed — and on one occasion the two disagreed, correctly.
cap.set(cv2.CAP_PROP_FOURCC, YUY2) # 1920x1080
h = blake2b(frame.tobytes()).digest()
# two reads of one output frame are bit-identical
# two different frames differ by sensor noise alone
# (~1.35 LSB/px over 2.07 M px) - no threshold,
# no moving target needed
scripts/measure_output_rate.py
EO panorama — two banks
33 ms
188
67 ms
55
100 ms
37
133 ms
7
200 ms
1
EO panorama — three banks
33 ms
274
67 ms
55
100 ms
22
133 ms
0
200 ms
0
How long each frame stayed on screen. The long stalls disappear; most frames move to the full 33 ms cadence.
What the third output bank changed
Two banks
Three banks
Change
EO panorama (main branch)
17.7 fps
22.3 fps
+26%
EO panorama (IR-DDR branch)
19.7 fps
22.9 fps
+16%
EO single, IR single, IR panorama
30 fps
30 fps
unchanged
Three runs per side, alternating bitstreams on the same board minutes apart. The unchanged row is the control: whatever was already at source rate stayed there.

## Slide 11
REMAINING WORK
EO panorama: the one mode still short
22.9
published now
30
cameras deliver
78%
frames on the full
33 ms cadence
22%
slip by one or two frame periods
It is not the output stage, and it is not the cameras
Switching the EO cameras from triggered to free-running changed the rate by 0.5 fps — within the run-to-run spread. That removes the shared exposure trigger entirely, so the limit is internal. And the profile is not a mode stuck at half rate; it is a mode that mostly keeps up and intermittently misses.
The mechanism, and the fix
Render frame N
24.9 ms
Manager releases, then searches
serialised — starts only when the render ends
Render frame N+1
starts late
edge
0.0
20.0
40.0
60.0
80.0
milliseconds
An EO panorama render needs a matched frame from all six cameras. The frame-set manager holds that set until the render completes, then walks four bank slots with a handshake to each camera before it can look for the next matched set. None of it overlaps the render. Acquiring the next set while the current render is still running is the targeted fix.

## Slide 12
PROVENANCE
Basis of every figure
Measured on hardware
Frame rates: SDI output grabbed at 60 fps, distinct frames counted by exact hash. 2026-08-20, build 00e0c57.
Render and publish latency: in-fabric probe on a ui_clk/64 tick, read over JTAG. 2026-08-19, build 67955bc.
How often the worst case occurs: counted from the on-screen dwell distribution, same optical capture.
Design constants
Output raster 1920x1080p30 - one frame period is 33.333 ms.
Capture-plus-scan-out geometry sums to exactly one frame period for every row; verified over all 1080 rows, spread 0.00 ms.
Render start windows read from the RTL: 1.95 ms per camera frame for IR panorama, matched six-camera set for EO panorama.
Limits and exclusions
Camera sensor and ISP delay excluded throughout - vendor specification.
Latency and frame rate come from different builds and different days; each is labelled. The three-bank change improves EO panorama's rate and was not re-measured for latency.
Row cancellation is exact for the single-camera modes and approximate for the panoramas, bounded by the row-window span (under 0.5 ms).
Not claimed: a certified sensor-to-display figure. Everything here is bounded by what can be observed at the camera interface and at the SDI output. An end-to-end number would need an external optical reference - a pulsed source into the lens and a photodiode on the display - which has not been run.