## Slide 1
Latency and Frame Rate
Six-camera EO / IR panorama · V19 Milestone 1
Measured three independent ways: the RTL and its simulation, an in-fabric timing probe read over JTAG, and the SDI output captured and analysed frame by frame.
RTL + simulation
ILA / in-fabric probe
Optical capture (Python)
2026-08-20

## Slide 2
SUMMARY
What the system does today
30
frames/s published
IR single
30
frames/s published
IR panorama
30
frames/s published
EO single, all six
22.9
frames/s published
EO panorama
71 ms
capture to display
EO panorama, best
Latency is a fixed number per mode, not a range
Every row of the picture has the SAME capture-to-display latency. A row captured early waits longest for its frame to complete, and is then scanned out first; a row captured last waits least and is scanned out last. The two offsets cancel exactly. This is shown on the next slide and is the reason no "typical" figure appears anywhere in this deck: there is no spread to average over.
Where the remaining work is
Seven of the eight measured configurations publish at the rate their cameras produce. EO panorama publishes 22.9 against a 30 fps source: 78% of its frames arrive on the full 33.3 ms cadence and 22% slip by one or two frame periods.

## Slide 3
THE KEY PICTURE
Why the stages must not be added up
Capture, render and scan-out overlap. Drawn end to end they read as 105 ms; drawn against one clock they are 71.5 ms.
0.0
33.3
66.7
100.0
milliseconds — one shared clock
Display frame edges
Camera exposes and transfers
frame N row 0 first → row 1079 last
FPGA aligns, renders, writes
align + render into a free bank
Published on the next edge
Display scans the frame out
row 0 first → row 1079 last
frame complete
published
row 0 → 71.5 ms
row 1079 → 71.5 ms
same length,
different start
The arithmetic. For row r of N: age when the frame completes = (1 − r/N) × 33.3, scan-out position = (r/N) × 33.3. These sum to 33.3 for every r — the row that waits longest to be captured is displayed first. Total = 33.3 + render-and-publish, identical for every row. Checked over all 1080 rows: spread 0.00 ms.
Notes: Exact for the single-camera modes, where output row r comes from source row r. In the panorama modes the warp lets a source row land within a band of output rows, so the cancellation is approximate - bounded by the row-window span of about 13 source rows, under 0.5 ms.

## Slide 4
MEASURED
Latency: best case and worst case
A finished frame may only be published on a display frame edge, and the camera does not track the display. The wait for that edge is anywhere from nothing to a full frame period, and that is the entire difference between the two columns.
Mode
Render occupancy
(ILA, untriggered)
Frame → render done
= fixed wait + render
BEST CASE
capture → display
WORST CASE
capture → display
Publishing
EO single
~8.4 ms
10.1 ms
43.4 ms
76.8 ms
29.75 fps
EO panorama
~24.9 ms
38.2 ms
71.5 ms
104.9 ms
22.9 fps
IR single
not measured
25.8 ms
59.1 ms
92.5 ms
30.01 fps
IR panorama
~26.6 ms
41.6 ms
59.9 ms
93.3 ms
29.97 fps
Why 41.6 ms does not cap throughput at 24 fps
The middle column is a latency, not an occupancy. It is a fixed phase wait plus the render, for IR panorama, about 15 ms of waiting for the row window to open, then a 26.6 ms render.
Only the render occupies the engine, and 26.6 ms fits inside 33.3 ms. The wait is a constant offset: it delays every frame equally and costs nothing per frame. Renders never overlap, so throughput is set by the occupancy alone.
Why the worst case occurs
The render finishes at some moment inside the display's 33.3 ms cycle and cannot choose that moment. Finish just before an edge and the frame goes out at once; finish just after one and it is held a whole further period.
This is a continuous drift, not an occasional fault, caused by fractional frequencies mismatches, which is why no single "typical" value is quoted. Shortening the render moves both columns down; locking the camera to the display raster would collapse them to one.
Notes: The IR panorama reference event read 15 Hz in that capture where the genlock says 30 - already recorded as untrustworthy in MEASURED_20260819. Re-measuring latency on the IR-DDR branch needs the timing probe ported to it; that branch has never carried it.

## Slide 5
MECHANISM
Best and worst, drawn on the same clock
Identical camera, identical render. The only difference is where the display's edge grid happens to fall — which nothing in the system controls.
BEST CASE — the render lands just before an edge
Display edges
Camera frame N
Align + render
38.2 ms
On screen
71.5 ms after capture
published
WORST CASE — the same render lands just after one
Display edges
Camera frame N
Align + render
38.2 ms — the same
Held, then on screen
held a whole frame period
104.9 ms after capture
edge missed by 0.35 ms
next edge
0.0
33.3
66.7
100.0
133.3
With the earlier two-bank output framebuffer a missed edge cost more than a late frame: the frame waiting to be published also blocked the NEXT render from starting, so one miss threw away a whole camera frame and the mode settled at half rate. The third output bank removes that blocking - the render behind it now proceeds regardless.

## Slide 6
OPTICAL EVIDENCE
Frame rate, measured off the SDI output
Grab the output at 60 fps, hash each frame, and count how often the picture changes. Repeat runs of 2 mean 30 fps; runs of 4 mean 15.
Mode
Camera delivers
New frames/s on screen
Repeat-run distribution
Verdict
IR single
30
29.81
2 × 352
at source rate
IR panorama
30
29.97
2 × 359
at source rate
EO single cam 1
30
29.89
2 × 357
at source rate
EO single cam 2
30
29.06
2 × 337, 4 × 11
at source rate
EO single cam 3
30
29.23
2 × 344, 4 × 5
at source rate
EO single cam 4
30
29.56
2 × 349, 4 × 5
at source rate
EO single cam 5
30
29.73
2 × 356, 4 × 2
at source rate
EO single cam 6
30
29.56
2 × 351, 4 × 4
at source rate
EO panorama
30
22.90
2 × 274, 4 × 55, 6 × 22
22% of frames slip

## Slide 7
WHERE THE LIMIT WAS WRITTEN
Evidence 1 — the RTL
The output framebuffer held two banks. A finished frame occupied one until it was displayed, and the rule below refused to start another render until then.
wire [2:0] out_bank_busy =
(1 << rd_bank) |
(pending_valid ? (1 << pending_bank) : 0);
// three banks, so a free one always exists
Why that rule cost a whole frame rather than a few milliseconds
A render cannot be started whenever convenient — its start is locked to the source. For IR panorama the renderer reads the live camera line caches, so it may only begin while the row gate is satisfied:
wire row_window_ok = (rows_max <= gate_min_row + 30);
wire row_ready_now = (rows_min >= need_row) && row_window_ok;
// rows 34..64 of 512 -> 1.95 ms, once per 33.3 ms camera frame
Miss that 1.95 ms window and the next chance is a full camera frame away. That is how a few milliseconds of commit delay turned into exactly half rate.
src/PanoramaBase_DdrBlackFrame.v and src/IrV19StreamingRenderer.v. The third bank required moving one address region; it was moved by exactly 8100 × 128 addresses so every camera keeps its DRAM bank assignment.

## Slide 8
ILA
Evidence 2 — the in-fabric timing probe
An ILA window is 8.8 µs and carries no timestamps, so a 33 ms interval cannot be recovered from a capture however it is triggered. The intervals are therefore measured in the FPGA and only the results are read out.
V19TimingProbe u_v19_timing (
.in_frame_ev (camera frame available),
.copy_start_ev(render begins),
.copy_done_ev (render complete),
.commit_ev (published to the display),
.out_edge_ev (output raster boundary));
// tick = ui_clk / 64 = 274.2 ns, 24 bits = 4.6 s
Measured intervals
Mode
frame → render done
(wait + render)
frame → on screen
EO single
10.1 ms
16.4 ms
EO panorama
38.2 ms
41.1 ms
IR single
25.8 ms
50.1 ms
IR panorama
41.6 ms
45.0 ms
Two ways this measurement lied before it was trusted
A capture triggered on activity cannot see idleness
Arming the ILA on "render active" reported the render occupying 84% of every frame. Sampling with no trigger condition at all gave 25-40%. Every duty figure in this deck is from an untriggered capture.
An interval register reports the LAST interval, not a rate
A pipeline that has stopped keeps reporting whatever it last managed - one stalled mode read as a healthy 33.3 ms while publishing nothing. Rates here are counted over a wall-clock gap, or measured optically, never read from an interval.
src/V19TimingProbe.v, calibrated against known intervals in sim/tb_V19TimingProbe.v — 10 of 10 checks pass. Captures via scripts/capture_v19_untriggered.tcl.

## Slide 9
PYTHON / OPTICAL
Evidence 3 — the output, analysed frame by frame
A python script analyze the frames on the input and counts the distinct/unique frames per second. The results are included The FPGA counter says a frame was published. Only this says the picture actually changed — and on one occasion the two disagreed, correctly.
cap.set(cv2.CAP_PROP_FOURCC, YUY2) # 1920x1080
h = blake2b(frame.tobytes()).digest()
# two reads of one output frame are bit-identical
# two different frames differ by sensor noise alone
# (~1.35 LSB/px over 2.07 M px) - no threshold,
# no moving target needed
scripts/measure_output_rate.py
200 ms
274
EO panorama
33 ms
67 ms
55
100 ms
22
133 ms
0
0
How long each frame stayed on screen. The long stalls disappear; most frames move to the full 33 ms cadence.
Mode | New frames/s on screen
IR single | 29.81
IR panorama | 29.97
EO_Single | 29.89
EO_Panorama | 22.90
The instrument was checked before the results were believed. A USB3 capture card can duplicate or drop frames on its own. IR single returns repeat runs of exactly 2 at a 59.9 fps grab, 352 times in a row, so the card resolves 30 distinct frames per second cleanly. Lower resolution and MJPEG change nothing. A duplicate would hash the same and count once; a dropped frame would make this under-count, never over-count.